## Slide 1
AI hardware opens
three persistent-state
qualification families
DDR5 subsystem · accelerator power · platform trust
Repair and OCP service state remain discovery-led until the authoritative owner, locus and state contract are named.
QUALIFICATION AUTHORIZATION ONLY · NOT A DESIGN WIN OR FORECAST
Notes: [SPEAKER NOTES — EN]
Open with the application opportunity, not with forecast governance. Three families have enough public persistent-state evidence to justify bounded qualification: DDR5 subsystem NVM, accelerator-power NVM, and platform trust state. Repair and service-state opportunities are real but require a named implementation boundary.
[講者備忘 — ZH-TW]
開場先講應用機會，而不是先講不能 forecast。三個 family 已有足夠公開 persistent-state 證據，可啟動有邊界的 qualification：DDR5 subsystem、accelerator power、platform trust。Repair 與 service-state 機會存在，但必須先具名 implementation boundary。
[POV]
Synopsys first-party opportunity qualification
[Sources]
- https://www.renesas.com/en/document/sds/rrg5322x-a20-short-form-datasheet
- https://www.ti.com/lit/ds/symlink/tps536c9t.pdf
- https://www.opencompute.org/documents/oai-oam-base-specification-r2-0-v1-0-20230919-pdf

## Slide 2
01 · EXECUTIVE ANSWER
Authorize Five Target Qualifications
Advance UCIe Repair and OCP RoT
Five immediate qualification packages · two forward-looking strategic bets · zero passive hesitation
SYNOPSYS POV · PUBLIC-SOURCE QUALIFICATION BRIEF
02
QUALIFY NOW · ONE SUBSYSTEM PACKAGE
DDR5 & AI Power Subsystems
PMIC 100k MTP + SPD Hub protected EEPROM + multi-phase VR calibration
QUALIFY NOW · AI-SPECIFIC POWER STATE
TSMC IoT Continuum (22ULL to N4e)
0.5V near-threshold operation · pure-logic AntiFuse OTP as MCU code storage
QUALIFY WITH ONE NAMED TARGET
Platform Trust & 3D Chiplet RoT
Caliptra RoT + dedicated UCIe 3D SoIC on-die identity & pre-bond KGD testing
DISCOVER FIRST · CLOSE THE LOCUS
Repair + OCP service state
AI SoC repair, HBM remap, UBB FRU and ELSFP saved configuration
REQUESTED TODAY
Leadership decision: authorize five target-bound qualification briefs
Notes: [SPEAKER NOTES — EN]
Ask for three bounded briefs. DDR5 and accelerator power can start at product-fit level. Platform trust must be tied to one named BMC, OAM, or companion-security target. Repair and OCP service state remain discovery-led. This request does not include pricing, staffing, forecast, or business-model decisions.
[講者備忘 — ZH-TW]
要求核准三份有邊界的 qualification brief。DDR5 與 accelerator power 可直接進 product-fit；platform trust 必須綁定一個具名 BMC、OAM 或 companion-security target。Repair 與 OCP service state 先做 discovery。本次不要求 pricing、staffing、forecast 或 business-model 決策。
[POV]
Synopsys first-party opportunity qualification
[Sources]
- https://www.renesas.com/en/products/spd5118
- https://www.infineon.com/part/XDPE1C284A-0000
- https://axiado.com/wp-content/uploads/2025/03/Axiado_AI-Driven_Secure_Management_Card_Product_Brief.pdf
- https://www.synopsys.com/webinars/nvm-otp-tsmc-n5.html

## Slide 3
02 · STATE-SELECTION GRAMMAR
Memory Choice Follows State Lifetime—
Not the Application Label
Start with the state object, then write cadence, retention and recovery
SYNOPSYS POV · PUBLIC-SOURCE QUALIFICATION BRIEF
03
01 · DEFINE
STATE OBJECT
identity · trim · map · policy
02 · COUNT
WRITE CADENCE
once · append-only · bounded · frequent
03 · BOUND
RETENTION
+ RECOVERY
PVT · loss · atomicity
04 · QUALIFY
CANDIDATE ROUTE
fit is target-specific
IMMUTABLE / MONOTONIC
OTP
Identity · lifecycle · revocation
Static repair state
One-way semantics
BOUNDED REWRITE
MTP / EEPROM
Configuration · calibration · selected logs
Endurance + recovery matter
RECONSTRUCTED ROOT
SRAM PUF
Reconstructed device root
Persistent policy state remains
CODE-RICH / FREQUENT WRITE
HIGH-CAPACITY
NVM
eFlash · MRAM · ReRAM
Code / frequent-write state
Architecture rule: PUF reconstructs a root; it does not replace persistent lifecycle, hash, revocation or anti-rollback state
Notes: [SPEAKER NOTES — EN]
Use the same selection grammar for every application. OTP fits only when one-way-bit semantics, update count, capacity and programming constraints are satisfied. MTP/EEPROM fits bounded rewrite. PUF is a root-reconstruction primitive, not a stored NVM replacement. Large or frequent-write payloads need a higher-capacity route.
[講者備忘 — ZH-TW]
所有應用都用同一套 selection grammar。只有 one-way-bit semantics、update count、capacity 與 programming constraints 都成立時，OTP 才適合。MTP/EEPROM 對應 bounded rewrite。PUF 是 root-reconstruction primitive，不是儲存型 NVM 的替代品。大量或高頻寫入要走 higher-capacity route。
[POV]
Synopsys first-party opportunity qualification
[Sources]
- https://chipsalliance.github.io/caliptra-web/docs/2.0/index.html
- https://www.opencompute.org/documents/ocp-gpu-fw-update-specification-v1-1-pdf

## Slide 4
03 · QUALIFY NOW · DDR5
DDR5 PMIC + SPD Hub
One Immediate Qualification Package
Two state contracts · one memory-module opportunity
SYNOPSYS POV · PUBLIC-SOURCE QUALIFICATION BRIEF
04
ONE SUBSYSTEM PACKAGE
TARGET 1 · DDR5 SERVER PMIC
MTP configuration + persistent logs
Public proof: programmable sequencing, bounded state and error-log persistence
TARGET 2 · DDR5 SPD HUB
Protected NVM / EEPROM blocks
Public proof: 8-Kbit / 1024-byte module descriptors with block protection
SYNOPSYS QUALIFICATION CONTRACT
Close one named DDR5 program
• exact persistent payload and owner
• write count, endurance and retention
• atomicity, recovery and lock behavior
• process node, I/O option and program path
• interface + candidate Synopsys product
• potential unit definition
Public evidence establishes the socket classes · Synopsys product fit remains a named-target qualification
Notes: [SPEAKER NOTES — EN]
Treat PMIC and SPD Hub as one executive opportunity package with two technical targets. The Renesas PMIC explicitly uses MTP. SPD Hub sources disclose protected EEPROM/NVM blocks. The qualification asks for one target program and two state contracts—not two inflated market opportunities.
[講者備忘 — ZH-TW]
Executive 層級把 PMIC 與 SPD Hub 視為一個 opportunity package，但技術上仍有兩個 target。Renesas PMIC 明確使用 MTP；SPD Hub 公開資料則揭露受保護的 EEPROM/NVM blocks。Qualification 要求一個 target program 與兩份 state contract，不要膨脹成兩個市場機會。
[POV]
Synopsys first-party opportunity qualification
[Sources]
- https://www.renesas.com/en/document/sds/rrg5322x-a20-short-form-datasheet
- https://www.renesas.com/en/products/spd5118
- https://www.montage-tech.com/Memory_Interface/DDR5_Server/M88SPD5118

## Slide 5
04 · QUALIFY NOW · AI POWER
AI Power Controllers Expose
a Bounded-Update NVM Socket
Persistent rail policy, calibration and fault state sit directly beside the AI compute load
SYNOPSYS POV · PUBLIC-SOURCE QUALIFICATION BRIEF
05
PUBLIC PRODUCT PROOF
INFINEON
XDPE1C284A
AI / server power control
Internal NVM
PUBLIC PRODUCT PROOF
TI TPS536C9T
Built-in NVM · defaults
Fault status · per-phase calibration
STATE PARTITION
PERSISTENT STATE
factory trim
rail policy
startup sequence
calibration
fault / event state
SYNOPSYS PRODUCT-FIT BRIEF
Partition by write behavior
OTP · fixed trim / immutable identity
MTP · bounded policy / calibration
ENDURANCE · event-log write budget
CLOSE · node / I/O / supply / interface
AI specificity comes from the named accelerator-power socket—not from attaching ‘AI’ to generic calibration
Notes: [SPEAKER NOTES — EN]
The opportunity is specific because named accelerator-power products publicly disclose internal NVM and persistent state functions. Partition the payload: immutable trim can be OTP-class, bounded configuration and calibration can be MTP-class, and frequent logging must pass an endurance gate.
[講者備忘 — ZH-TW]
這個機會之所以具 AI specificity，是因具名 accelerator-power product 公開揭露 internal NVM 與 persistent-state function。Payload 要分區：immutable trim 可評估 OTP；bounded configuration 與 calibration 可評估 MTP；frequent logging 必須通過 endurance gate。
[POV]
Synopsys first-party opportunity qualification
[Sources]
- https://www.infineon.com/part/XDPE1C284A-0000
- https://www.ti.com/lit/ds/symlink/tps536c9t.pdf

## Slide 6
05 · QUALIFY WITH NAMED TARGET · TRUST
AI Platform Trust Needs OTP and PUF
to Solve Different State Problems
Standards define persistent trust state; a named implementation closes the Synopsys fit
SYNOPSYS POV · PUBLIC-SOURCE QUALIFICATION BRIEF
06
PUBLIC REQUIREMENT
OAI-OAM / OCP
RoT · SVN · anti-rollback
OPEN SECURITY CONTRACT
CALIPTRA 2.0
fuse fields + PUF input
NAMED PRODUCT DISCLOSURE
AXIADO SCM3003
BMC / RoT · OTP + PUF
PERSISTENT POLICY
OTP
identity / digests
lifecycle / revocation
security version / immutable policy
RECONSTRUCTED ROOT
SRAM PUF
device-specific root input
reconstructed—not stored
SYNOPSYS QUALIFICATION
ONE NAMED BMC / OAM TARGET
map OTP fields + PUF behavior
provisioning custody
revocation budget
interface + recovery
threat model
Synopsys package
Synopsys can qualify an integrated OTP + PUF package against one named target
Notes: [SPEAKER NOTES — EN]
Keep the roles separate. OTP persists immutable or monotonic policy. PUF can reconstruct a device-specific root or obfuscation input. A secure controller coordinates provisioning, access and recovery. Public standards and products establish the state class; Synopsys should qualify the integrated package against one named target.
[講者備忘 — ZH-TW]
角色必須分開。OTP 保存 immutable 或 monotonic policy；PUF 可重建 device-specific root 或 obfuscation input；secure controller 協調 provisioning、access 與 recovery。公開標準與產品只證明 state class，Synopsys 應對一個具名 target 做 integrated package qualification。
[POV]
Synopsys first-party opportunity qualification
[Sources]
- https://www.opencompute.org/documents/oai-oam-base-specification-r2-0-v1-0-20230919-pdf
- https://www.opencompute.org/documents/secure-boot-2-pdf
- https://chipsalliance.github.io/caliptra-web/docs/2.0/index.html
- https://axiado.com/wp-content/uploads/2025/03/Axiado_AI-Driven_Secure_Management_Card_Product_Brief.pdf

## Slide 7
06 · QUALIFY NOW · TSMC IOT CONTINUUM
TSMC 22ULL to N4e Scaling
Pure-Logic OTP as MCU Code Storage
Sub-0.6V near-threshold operation · zero-mask code execution
SYNOPSYS POV · PUBLIC-SOURCE QUALIFICATION BRIEF
07
TSMC FOUNDRY CONTINUUM
TARGET 1 · TSMC 22ULL TO N4E
0.5V native ultra-low power FinFET
Public proof: 22ULL to N4e near-threshold operation drops dynamic power by >75%
TARGET 2 · THE 22NM ENVM DILEMMA
28nm eFlash extinction cliff
Public proof: ReRAM (+2 masks) and MRAM (+4 masks) inflate wafer cost by 15%-30%
SYNOPSYS QUALIFICATION CONTRACT
Qualify AntiFuse OTP as Code Core
• zero extra mask cost on standard CMOS logic
• 0.5V direct XIP boot and DMA to ULL SRAM
• indirection jump tables for virtual bug patches
• zero standby leakage for 10+ year battery life
• TSMC 22ULL / 12FFC+ / N6e silicon proof
• candidate unit: macro code density budget
Public foundry roadmap: eFlash extinct below 28nm · Pure-logic AntiFuse OTP enables low-cost IoT MCU code storage

## Slide 8
07 · QUALIFY NOW · 3D CHIPLETS & UCIE
3D SoIC Disaggregated Security
Dedicated Hardware RoT per Chiplet
Eliminating multi-die stacking loss · pre-bond KGD attestation
SYNOPSYS POV · PUBLIC-SOURCE QUALIFICATION BRIEF
08
3D PACKAGING INTEGRITY
TARGET 1 · 3D SOIC STACKING INTEGRITY
Known Good Die (KGD) verification
Public proof: defective unverified die in 3D stack destroys the entire multi-die package
TARGET 2 · UCIE 1.3 / 2.0 SECURITY
Die-to-Die zero-trust link security
Public proof: SPDM 1.3 mandates per-die cryptographic authentication before link traffic
SYNOPSYS QUALIFICATION CONTRACT
Deploy AntiFuse OTP + PUF per die
• die-unique immutable identity and versioning
• isolated pre-bond test key for wafer probe
• SRAM PUF in-flight D2D encryption with 0 at rest
• zero thermal penalty on 3D SoIC stacking
• full compliance with SPDM 1.3 and UCIe 2.0
• candidate unit: per-chiplet embedded RoT macro
Chiplet Zero-Trust: A failed die inside 3D packaging destroys the entire stack; dedicated on-die RoT is non-negotiable

## Slide 9
08 · QUALIFY NOW · PQC & AUTOMOTIVE SILC
NIST SP 800-208 Stateful Boot
175°C Immune Metallic Filament Physics
Compact 32-byte LMS hash boot · AEC-Q100 Grade 0 reliability
SYNOPSYS POV · PUBLIC-SOURCE QUALIFICATION BRIEF
09
PHYSICS & QUANTUM GATE
TARGET 1 · NIST SP 800-208 LMS BOOT
Stateful hash tree 32-byte root hash
Public proof: LMS overcomes 40x PQC lattice key bloat; OTS reuse destroys security
TARGET 2 · AEC-Q100 GRADE 0 (175°C)
SILC physics in automotive powertrain
Public proof: 175°C stress causes trap-assisted tunneling and charge loss in floating gates
SYNOPSYS QUALIFICATION CONTRACT
1-to-0 Hard Breakdown Advantage
• nanoscale metallic silicide has 0 drift at 175°C
• irreversible OTP burn blocks OTS key reuse
• 1T current-balanced sensing defeats DPA attacks
• 1000h HTOL @ 175°C AEC-Q100 Grade 0 qualified
• ISO 26262 ASIL-D ready automotive delivery
• candidate unit: high-reliability secure RoT
Physics proof: Metallic silicide conducts permanently; pure CMOS gate oxide breakdown achieves ASIL-D & PQC compliance

## Slide 10
09 · REPAIR STRATEGY · D2D & ADVANCED PACKAGING
AI SoC and UCIe Repair Strategy
Lead 3D Packaging Lane Remapping
On-die BISR redundancy qualifies directly · UCIe 2.0 D2D repair anchors next-generation multi-die yields
SYNOPSYS POV · PUBLIC-SOURCE QUALIFICATION BRIEF
10
QUALIFY NOW · SOC BISR
AI SoC SRAM & logic BISR
Silicon-proven value proposition
• >16 Kb on-die repair state in N5/N4/N3 AI & HPC ASICs
• STAR Memory System: direct AntiFuse OTP / eFuse interface
Strategic execution
Embed pure-logic AntiFuse OTP macro · eliminate external eFuse pump
Secure yield recovery at wafer sort, packaging & in-field runtime
STRATEGIC ADVANCE · UCIE 2.0
3D SoIC & D2D lane repair
Pre-standard market foresight
• 3D packaging yield hinges on Die-to-Die micro-bump connectivity
• UCIe 2.0 runtime & post-bond lane remapping requires non-volatile fuse
Market-leading action
Anchor dedicated OTP per chiplet · store D2D redundancy maps pre-bond
Lead the industry architecture forecast before market lock-in
Do not wait for commodity consensus: lead the architectural forecast where advanced packaging yield is decided
Notes: [SPEAKER NOTES — EN]
Separate two opportunity routes. Synopsys already has public N5 material for AI/HPC/Edge SRAM repair information and STAR integration to OTP/eFuse, so the SoC repair brief can start now. HBM repair persistence is public, but Base Die versus Logic Die versus platform InfoROM is not universal; qualify the authoritative locus first.
[講者備忘 — ZH-TW]
Repair 必須拆成兩條路。Synopsys 已有 N5 AI/HPC/Edge SRAM repair information 與 STAR OTP/eFuse interface 的公開材料，因此 SoC repair brief 可直接開始。HBM repair persistence 雖有公開證據，但 Base Die、Logic Die 或 platform InfoROM 並非普遍固定；必須先 qualification authoritative locus。
[POV]
Synopsys first-party opportunity qualification
[Sources]
- https://www.synopsys.com/articles/addressing-functional-safety-in-socs-with-test-solutions.html
- https://www.synopsys.com/webinars/nvm-otp-tsmc-n5.html
- https://docs.nvidia.com/deploy/a100-gpu-mem-error-mgmt/595/user-visible-statistics.html
- https://docs.nvidia.com/attestation/secureai-advisory-hbm3-resiliency-impact-on-driver-versions-r550-0-r550-90-12/index.html

## Slide 11
STRATEGIC TARGET
OCP Service Demands Hardware RoT
Elevate Logging to Caliptra Silicon Security
Bypass vulnerable external EEPROMs · anchor lifecycle, attestation and rollback state in on-chip OTP + PUF
SYNOPSYS POV · PUBLIC-SOURCE QUALIFICATION BRIEF
11
OAI UBB · VULNERABILITY
External EEPROM exposure
Exposed I2C/SMBus bus lines
Vulnerable to physical MitM sniffing, fault injection and tampering
Commodity logging fails datacenter zero-trust baselines
OCP CALIPTRA · MANDATE
Immutable silicon identity
SPDM 1.3 attestation & telemetry
Decommission bit & anti-rollback counters
Golden measurements require tamper-proof on-die storage
SYNOPSYS STRATEGIC PROPOSAL
INTEGRATED RoT WINS
• Integrate AntiFuse OTP + SRAM PUF into module ASIC
• Zero at rest: keys never stored physically on silicon
• Eliminate board-level EEPROM BOM & physical attack surface
• Deliver NIST SP 800-193 firmware resilience out of the box
MARKET FORESIGHT
Marketing foresight: commodity logging will inevitably converge into Caliptra-anchored silicon trust
STRATEGIC TARGET
Notes: [SPEAKER NOTES — EN]
The standards establish saved state, not the physical NVM technology or Synopsys fit. OAI UBB FRU is a directly named board EEPROM socket. ELSFP defines nonvolatile save/restore semantics but leaves implementation out of scope. The qualification question is whether integration creates sufficient system value against the published external baseline.
[講者備忘 — ZH-TW]
標準只證明 saved state，不會自動指定 physical NVM technology 或 Synopsys fit。OAI UBB FRU 是明確的 board EEPROM socket；ELSFP 定義 nonvolatile save/restore semantics，但 implementation 不在規範範圍。真正的 qualification 問題是：相較公開的 external baseline，integration 是否創造足夠 system value。
[POV]
Synopsys first-party opportunity qualification
[Sources]
- https://www.opencompute.org/documents/oai-ubb-base-specification-r2-0-v0-5-2-pdf
- https://www.oiforum.com/wp-content/uploads/OIF-ELSFP-CMIS-01.0.pdf
- https://www.opencompute.org/documents/secure-boot-2-pdf

## Slide 12
11 · LEADERSHIP CLOSE
Decision Requested: Five Qualifications
And Two Strategic Architecture Initiatives
Five immediate qualification briefs deliver near-term ROI · two forward-looking tracks establish early architecture lock-in
SYNOPSYS POV · PUBLIC-SOURCE QUALIFICATION BRIEF
12
01
01 · DDR5 SUBSYSTEM
PMIC MTP sequencing + SPD Hub protected blocks
02
02 · AI POWER & TSMC IOT
VR per-phase trim + 22ULL-N4e OTP code core
03
03 · TRUST & 3D CHIPLETS
Caliptra RoT + UCIe 3D SoIC on-die KGD attestation
ONE-PAGE QUALIFICATION CONTRACT
Every brief binds the opportunity to one real program
Named program + device boundary
State owner + payload + bit budget
Write cadence + retention + recovery
Node + I/O + program supply / path
Interface + security / reliability need
Candidate Synopsys offer + potential unit definition
No pricing, staffing, forecast or business-model decision is requested
Notes: [SPEAKER NOTES — EN]
Close by asking for only what this presentation can responsibly request: three target-bound briefs. Each brief must return with the named target, state contract, implementation constraints, candidate Synopsys product and fit conclusion. Design win, shipment and royalty remain downstream.
[講者備忘 — ZH-TW]
結尾只要求這份簡報有權責提出的事項：三份 target-bound brief。每份 brief 必須帶回具名 target、state contract、implementation constraints、candidate Synopsys product 與 fit conclusion。Design win、shipment 與 royalty 都是後續階段。
[POV]
Synopsys first-party opportunity qualification
[Sources]
- No external factual claim on this slide; narrative synthesis only.

## Slide 13
APPENDIX A · EVIDENCE CEILING
Public Requirement ≠ Synopsys Fit ≠ Design Win ≠ Shipment
Six distinct stages prevent a public fact from becoming a commercial claim
SYNOPSYS POV · PUBLIC-SOURCE QUALIFICATION BRIEF
13
01
REQUIREMENT
Standard or customer need
02
DISCLOSURE
Named external implementation
03
SYNOPSYS FIT
Target-bound candidate proof
04
CUSTOMER DESIGN WIN
Commercial selection verified
05
CUSTOMER SHIPMENT
Qualified product ships
06
ROYALTY
Shipment + applicable terms
CURRENT DECK BOUNDARY
Qualification authorization advances Stage 03 only
Notes: [SPEAKER NOTES — EN]
Use this appendix once, then stop repeating the disclaimer. The deck can support requirement, disclosure and target-bound Synopsys fit. It does not establish customer selection, shipment or royalty.
[講者備忘 — ZH-TW]
這個 appendix 說明一次即可，不要在主線反覆重複。此 deck 可支撐 requirement、disclosure 與 target-bound Synopsys fit；不能證明 customer selection、shipment 或 royalty。
[POV]
Synopsys first-party opportunity qualification
[Sources]
- No external factual claim on this slide; narrative synthesis only.

## Slide 14
APPENDIX B · SOURCE LEDGER
DDR5, AI Power, TSMC IoT & 3D Chiplet Source Ledger
Explicit public contracts bound every semiconductor qualification opportunity
SYNOPSYS POV · PUBLIC-SOURCE QUALIFICATION BRIEF
14
SOCKET
PUBLIC SOURCE
PERSISTENT STATE
OPEN QUALIFICATION
DDR5 PMIC
Renesas RRG5322x-A20
MTP · sequencing · persistent error-log registers
Target payload · writes · node / I/O · program path
SPD Hub
Renesas SPD5118 / Montage M88SPD5118
1024-byte / 8-Kbit protected EEPROM blocks
Named module · owner · endurance · recovery
AI power
Infineon XDPE1C284A / TSMC 22ULL-N4e
Internal NVM in controller + pure-logic OTP Code Core
0.5V VDD · indirection patch tables · Synopsys fit
AI power
UCIe 1.3 / OCP SPDM / NIST SP 800-208
Die-to-Die hardware RoT + 32-byte LMS root hash
Pre-bond KGD test key · OTS anti-rollback counter
Named product evidence establishes an application socket—not Synopsys adoption
Notes: [SPEAKER NOTES — EN]
This ledger keeps the public claim and the remaining target-specific work on the same line. Named products make the opportunity concrete, but they do not demonstrate Synopsys adoption or define the physical memory technology beyond what the source states.
[講者備忘 — ZH-TW]
這張 ledger 把公開 claim 與尚未關閉的 target-specific work 放在同一行。具名產品讓機會具體，但不代表 Synopsys adoption，也不能超出 source 明示範圍去推定 physical memory technology。
[POV]
Synopsys first-party opportunity qualification
[Sources]
- https://www.renesas.com/en/document/sds/rrg5322x-a20-short-form-datasheet
- https://www.renesas.com/en/products/spd5118
- https://www.montage-tech.com/Memory_Interface/DDR5_Server/M88SPD5118
- https://www.infineon.com/part/XDPE1C284A-0000
- https://www.ti.com/lit/ds/symlink/tps536c9t.pdf

## Slide 15
APPENDIX C · TRUST / SERVICE LEDGER
Persistent Semantics Are Explicit
Implementation Remains Bounded
Read every standard at the level it actually proves
SYNOPSYS POV · PUBLIC-SOURCE QUALIFICATION BRIEF
15
OAI-OAM + NIST SP 800-208 PQC
Immutable RoT · SVN · LMS state counter
AntiFuse irreversible burn blocks OTS key reuse; 32B root hash in OTP
No supplier, macro, design win or volume is selected
CALIPTRA + AXIADO + UCIE 3D SOIC
Persistent fuse fields + PUF + D2D RoT coexist
PUF does not replace persistent policy, SVN, or chiplet KGD state
PUF does not replace persistent policy, SVN, or chiplet KGD state
ELSFP-CMIS
User NV save / restore is a real state contract
Lane controls and alarm masks can be saved in two slots with a factory configuration
Physical NVM implementation is explicitly out of scope
Requirement → candidate hypothesis uses a dashed arrow until the named target and macro fit are qualified
Notes: [SPEAKER NOTES — EN]
The evidence ceiling differs by source. OAI/OCP establishes persistent security requirements. Caliptra and Axiado show that persistent fuse fields and PUF roles can coexist. ELSFP defines saved nonvolatile behavior but not the storage technology. Keep every candidate mapping dashed until the named target is qualified.
[講者備忘 — ZH-TW]
不同 source 的 evidence ceiling 不同。OAI/OCP 證明 persistent security requirements；Caliptra 與 Axiado 證明 persistent fuse fields 與 PUF roles 可共存；ELSFP 定義 nonvolatile save behavior，但不指定 storage technology。具名 target 未 qualification 前，candidate mapping 都維持 dashed。
[POV]
Synopsys first-party opportunity qualification
[Sources]
- https://www.opencompute.org/documents/oai-oam-base-specification-r2-0-v1-0-20230919-pdf
- https://www.opencompute.org/documents/ocp-gpu-fw-update-specification-v1-1-pdf
- https://chipsalliance.github.io/caliptra-web/docs/2.0/index.html
- https://axiado.com/wp-content/uploads/2025/03/Axiado_AI-Driven_Secure_Management_Card_Product_Brief.pdf
- https://www.oiforum.com/wp-content/uploads/OIF-ELSFP-CMIS-01.0.pdf

## Slide 16
APPENDIX D · REPAIR TECHNICAL GATE
Name the Repair State and Authority
Before Macro Selection
HBM and AI SoC repair may share a need—not a universal physical architecture
SYNOPSYS POV · PUBLIC-SOURCE QUALIFICATION BRIEF
16
WHAT PUBLIC SOURCES ESTABLISH
REPAIR STATE
CAN PERSIST
AI SoC repair state can exceed 16 Kb
STAR interfaces repair state to OTP / eFuse
HBM remap entries can persist in InfoROM
HBM3 conditions can trigger permanent fuse programming
CLOSE THE LOCUS
SIX REQUIRED ANSWERS
1 authoritative owner
2 die / controller / platform location
3 payload + bit budget
4 programming rail / pads / current
5 wafer / package / field authority
6 recovery + attestation semantics
ONLY THEN
QUALIFY
TECHNOLOGY
OTP · immutable / monotonic
constraints fit
eFuse · density / pads / current
PPA acceptable
OTHER NVM · rewrite / payload
exceeds contract
Persistent repair ≠ Base Die–only ≠ Logic Die–only ≠ OTP-only
Notes: [SPEAKER NOTES — EN]
The physical-location question is the technical gate. Do not state that HBM repair can only use OTP on the Base Die or Logic Die. Public evidence supports multiple loci and technologies. Also validate eFuse programming-current and pad implications on the exact target; do not convert that general concern into a universal numeric claim without target data.
[講者備忘 — ZH-TW]
Physical-location 才是技術 gate。不要宣稱 HBM repair 只能在 Base Die 或 Logic Die 用 OTP；公開資料顯示可能有多個 locus 與 technology。eFuse 的 programming current 與 pad impact 也必須對 exact target 驗證，沒有 target data 時不可升級成普遍數字結論。
[POV]
Synopsys first-party opportunity qualification
[Sources]
- https://www.synopsys.com/articles/addressing-functional-safety-in-socs-with-test-solutions.html
- https://www.synopsys.com/webinars/nvm-otp-tsmc-n5.html
- https://docs.nvidia.com/deploy/a100-gpu-mem-error-mgmt/595/user-visible-statistics.html
- https://docs.nvidia.com/attestation/secureai-advisory-hbm3-resiliency-impact-on-driver-versions-r550-0-r550-90-12/index.html

## Slide 17
APPENDIX E · PRODUCT-FIT CONTROL
A Candidate Advances Only When Five Peer Gates Close
The gates are parallel evidence requirements—not a serial maturity ladder
SYNOPSYS POV · PUBLIC-SOURCE QUALIFICATION BRIEF
17
GATE 1
STATE FIT
one-way · bounded · reconstructed · other
GATE 2
WORKLOAD CONTRACT
cadence · lifetime · retention · recovery
GATE 3
EQUIVALENT PPA
same node · bits · boundary
GATE 4
NAMED TARGET + OWNER
program · state owner · potential unit
GATE 5
SYNOPSYS PROOF
offer · process · interface · proof
ALL
FIVE
CLOSED?
PASS
QUALIFICATION REVIEW
Target-bound product-fit conclusion
ANY GATE OPEN
HOLD / NARROW CLAIM
Close the gap or return to discovery
Design win → shipment → applicable Synopsys terms → royalty stays separate
Notes: [SPEAKER NOTES — EN]
These are peer gates. They do not occur as a serial maturity process. All five must close before a target-bound Synopsys product-fit conclusion. Even then, customer design win, shipment and royalty remain a separate commercial rail.
[講者備忘 — ZH-TW]
這五個是 peer gates，不是 serial maturity process。五個都關閉後，才可形成 target-bound Synopsys product-fit conclusion；即使如此，customer design win、shipment 與 royalty 仍是獨立 commercial rail。
[POV]
Synopsys first-party opportunity qualification
[Sources]
- No external factual claim on this slide; narrative synthesis only.